## Slide 1: Preventive maintenance with ultrasound

## Slide 2: Theory of ultrasound

## Slide 3: Frequency range of sound
sound
20 Hz
16 KHz/20 KHz
Infrasound
Ultrasound
Sound frequencies
Infrasound < 20 Hz.
Sound : between 20 Hz up to 20 kHz.
Ultrasound = > 20 kHz.

## Slide 4: Caracteristic of ultrasound
Ultrasound : concentrated energy around the propagation of the axis => Directionals.
Sound : energy dispersed around the propagation of the axis => Multidirectionals.

## Slide 5: Caracteristic of ultrasound
Ultrasound :
low energy
geometric dispersion
attenuation frequency/distance
Faster absorbed.

## Slide 6: Origins of ultrasound
Turbulences
  Leaks of air compressed, gas or vaccum
  Leaks of hydraulic circuit
  Leaks of steam circuit
Shocks and friction
  Bearings and gears
  Lubrication
  Pump cavitation
Partial discharges
  Corona effect
  Tracking
  Arcing

## Slide 7: Overview of the applications

## Slide 8: Applications
Air compressed/vaccum/gas
Steam traps/valves
Lubrication
Mechanical
Electrical
Control of tightness

## Slide 9: Applications
Lubrication
Mechanical
Electrical
Air compressed
vaccum/gas
Steam traps/valves
Energy saving program
Maintenance applications
Reduce the energy cost
Increase the avaibility of the rotating machines
 Preventive maintenance

## Slide 10: Applications
Control of thightness
Quality control

## Slide 11: Energy saving program

## Slide 12: Air compressed
The main application covered by the ultrasound
Precognized by the major actors of this market
  Atlas Copco
  Festo
  Kaiser
  Ingersoll Rand
ROI instantanous

## Slide 13: Air compressed
Consumption of the equipment | 43 %
Inappropriate use | 16 %
Purged air | 5 %
Faulty valves | 2 %
Leaks | 34 %
International average: from ADEME

## Slide 14: Air compressed
Without maintenance program of leaks detection, network losses is around 30 to 40 % of the total consumption.
With maintenance program of leaks detection, network losses is 5 % of the total consumption.

## Slide 15: Air compressed
3 reasons to do in priority a maintenance program to look for the leaks:
Low investment is required
The highest economy source
ROI very fast.

## Slide 16: Air compressed
International average: from ADEME

## Slide 17: Air compressed
Developped in collaboration with ATLAS COPCO

## Slide 18: Air compressed

## Slide 19: Air compressed

## Slide 20: Air compressed
Airbonne sensor in short distance (up to 2m) :
- Internal US sensor: close to the inspected element.
- Flexible rod: close and difficult acces zones
Sensor choice

## Slide 21: Air compressed
Airbonne sensor in medium distance (up to 5 m): internal sensor
+ EDS (Extended Distance Cone)
Sensor choice

## Slide 22: Air compressed
Airbonne sensor in long distance:
(5m up to 30 m)
Parabol dish
Sensor choice

## Slide 23: Steam traps
Precognized by the major actors of this market
  Spirax
  Armstrong
  TLV
  Blok
Easy to use
ROI very fast

## Slide 24: Steam traps
Steam traps are automatic valves which must open for draining condensate, air and CO2 and must be closed for maintaining live steam.
Reminder

## Slide 25: Steam traps
Failed close:
  Accumulating condensates, air and CO2
     Hammer shocks
     Installation dammage
Failed open
  Energy waste
     Energy overconsumption
     Deterioration in production quality.
     Efficiency drop = waste of money
Normal status
3 possibilities

## Slide 26: Steam traps
Cost of steam | 30€/T
Steam traps failed | 20-30 %
Cost of one steam trap failed open | 2.500€/an
International average: from Spirax Sarco
Key figures

## Slide 27: Steam traps
International average: from Spirax Sarco
Drain orifice  3mm
  4.000€/year at 6 bar
  6.500€/an at 10 bar
Example

## Slide 28: Steam traps
Examples

## Slide 29: Valves
If the valve is leaking, the valve seat measurement will be higher.
Collect a measurement upstream, valve seat and downstream.
Methodologies

## Slide 30: Valves: case strory
independent operator of the natural gas transmission infrastructure in Belgium

## Slide 31: Valves: case story
Upstream
Body.seat
Downstream
1st methodology: upstrean/body/downstream

## Slide 32: Valves: case story
Upstream
Body/seat
Downstream
21 dB/µV
10 dB/µV
8 dB/µV

## Slide 33: Valves: case story

## Slide 34: Applications of rotating machines

## Slide 35: Rotating machines
Two mechanical phenomena generated US:
  Shocks
  Friction
Several mechanical applications:
  Optimization of the lubrication
  Bearings low/high speed
  Gears
  Pump cavitation
Theorical

## Slide 36: Optimization of the lubrication
Ultrasound is a selective method highlighting bearing and lubrication failures.

## Slide 37: Optimization of the lubrication
Mechanical failures are due to improper lubrication. | 60%
Bearing failures are due to inappropriate lubrication. | 50%
Key figures

## Slide 38: Optimization of the lubrication
Over greased
Inadequate lubricant
Under lubricated
3 origins of the bearing failures

## Slide 39: Optimization of the lubrication
Example: perform a bearing lubrification

## Slide 40: Optimization of the lubrication
Must be re-lubricate?
Which quantity?
What is the periodicity of re-lubrication?
Ultrasound answers the 3 problems posed by lubrication:

## Slide 41: Optimization of the lubrication
ULTRASOUND MEASUREMENTS BEARING PULLEY SIDE |  | 
dB µV RMS | dB µV Peak | Actions
54,1 | 75,4 | Before lubrication
37,9 | 53,4 | After lubrication
Palier CA
Bearing Pulley side
Before
Lubrication
After
Lubrication
Fan Bearing Pulley side – After lubrication
Fan Bearing Pulley side – Before lubrication
Example

## Slide 42: Optimization of the lubrication
Example
Lubrication
After lubrication
Before lubrication
After lubrication
Shocks
Before lubrication
ULTRASOUND MEASUREMENTS BEARING END DRIVEN PUMP |  | 
dB µV RMS | dB µV Peak | Actions
15,2 | 31,5 | Before lubrication
17,3 | 36,5 | Lubrication
15,2 | 36 | After lubrication
Bearing non end driven
Bearing End Driven

## Slide 43: Optimization of the lubrication
ULTRASOUND MEASUREMENTS CRUSHER – ELECTRICAL MOTOR |  | 
dB µV RMS | dB µV Peak value | Location
31,9 | 51,5 | DE (Before lubrication)
18,7 | 42,3 | DE (Before lubrication)
26,3 | 51,3 | DE (After lubrication)
23,9 | 38,6 | NDE
Electrical motor DE – Before lubrication
Electrical motor DE – After lubrication
Electrical motor NDE
Electrical motor DE – After lubrification
Zone de chocs

## Slide 44: LUBExpert

## Slide 45: Optimization of the lubrication : LUBExpert

## Slide 46: Optimization of the lubrication: LUBExpert

## Slide 47: Bearings
1st step:
  Listening: simple, intuitive and quick
2nd step:
  Recording of the static measurement
     confirms listening
3rd step:
  Recording of the dynamic measurement
     confirms listening and static measurement

## Slide 48: Bearings: listening

## Slide 49: Bearings: static measurement
+6
+8
+16
Healthy bearing
Grease defect
Early stage failure
Irrversible failure

## Slide 50: Bearings: static measurement

## Slide 51: Bearings: dynamic measurement
GENERATOR DA1 – Bearing end driven
GENERATOR DA2 – Bearing end driven
 | dB µV (RMS)
Bearing DE DA1 | 47,1
Bearing DE DA2 | 24,9

## Slide 52: Slow bearings
Example: oven bearing 4 RPM
 | dB µV (RMS) | dB µV (Peak)
Bearing 1 | - 9,6 | 11,2
Bearing 2 | -9,7 | 15,8
Bearing 3 | 12,8 | 32,1
Bearing 4 | 14,2 | 32
Bearing 5 | -9,9 | 21,7
Bearing 6 | -10 | 7,5
Bearing 7 | -10,3 | 13
Bearing 8 | -6,8 | 30,5

## Slide 53: Gears
If ultrasound methodology let the control of the bearing, you can do also the gear control (gear boxes, multiplicator, …)
The dynamic measurements is recommanded on this case to identify the gear problem or bearing failure.

## Slide 54: Gear: Case story
KINEMATICS OF THE PUMP | 
PLANETARY GEAR BOXE | FREQUENCiES
Axial gear 21 teeth | 68,09 Hz
Solar gear 98 teeth | 4,86 Hz
Outer ring of gear 223 teeth | 6,41 Hz
Output speed 128,4 RPM | 2,14 Hz
Gearmesh frequency | 476,62 Hz
KINEMATICS OF THE PUMP | 
PUMP | FREQUENCiES
 | 1,03 Hz
Wheel 6 blades | 12,82 Hz

## Slide 55: Gear: case story
On the housing bearing 21R1 of the reducer, there is a regular shock with an interval of 0.1518 s, ie 6.58 Hz, which corresponds to the frequency of the outer ring of the gear.
This phenomenon could be related to a broken tooth of the outer gear.
It would be recommended to do a video endoscopy of the reducer.
Location 22R1 – Outer ring of the gear frequency

## Slide 56: Gear: case story
ULTRASOUND MEASUREMENTS OUTPUT SHAFT- 4 RPM |  | 
dB µV RMS | dB µV Peak Value | GEAR BOXE
7,4 | 34,7 | Right Mixer
1
2
3
4
5
1
Tour de rotation de l’arbre de sortie du réducteur
On the output shaft of the reducer there are two shocks at each rotation. Not having the exact frequencies of the kinematics of the reducer it is difficult to make an accurate diagnosis. It would seem that it would be a problem of teeth clearance (excessive or tight). To monitor
An inspection with an endoscope would be recommended.

## Slide 57: Gear: case strory
Example: planetary gear
Input speed: 11 RPM
Output speed: 2 RPM
BEARING 2 PLANETARY GEAR – INPUT LEFT
BEARING 2 PLANETARY GEAR – OUTPUT RIGHT

## Slide 58: Pump cavitation: listening
The cavitation is the steam bubbles forming du to pressure drop.

## Slide 59: Pump cavitation: listening
Cavitation of pump with immediate corrective action

## Slide 60: Applications of Partial discharges localisation

## Slide 61: Electrical inspection
The partial discharges produce the ultrasound
The detection and the analysis avoid the harmful consequencies of the security of the electrical installations and production

## Slide 62: 3 kind of defects
Corona:
  Air ionization
  Produces ozone and nitric acid (>2kV)
Tracking
  Moitsure and humidity
  Affects the surface of electrical components.
Arcing
  Plasma discharges

## Slide 63: Thightness control

## Slide 64: Thightness control
An ultrasound transmitter is located inside the area who you will perform the test. The transmitter floods the area of ultrasound. The ultrasound escapes by the holes, defect seals or cracks.
The technician checks outside of the area using SDT200 or SDT 270 like ultrasonic receiver, who detect, localize and measure the proportion of ultrasound who escape.

## Slide 65: Thightness control
Sectors:
  Industry : white rooms, refrigerated storage rooms, boilers, composite tanks…..
  Marine : hatchcover, weathertight and water tight door, wheelhouse…
  Automotive : acoustic transparency of the cars.
  Transport : trucks, bus, trains, airplanes, helicopters.
  Construction : roofs, door and windows.
  Military : submarine, space vehicles, armored vehicles, tank….
  Nuclear – intégrity of the wall between the reactor and outside.